## Slide 2: Introduction to the Water Quality Analysis Modeling System
WASP
Version 8.5
January 12-17 2026

## Slide 3: Logistics
Wi-Fi Access R4Conference 1 & 3
EPA Employees OneEPA
Workshop Structure
Start/End Times
Bathrooms
Break Rooms
Lunch

## Slide 4: Introductions
Instructors:
  Tim Wool – US EPA Region 4
  Robert Ambrose – US EPA ORD - Retired
  Christopher Knightes – US EPA ORD
Assistants
  Craig Hesterlee– US EPA Region 4
  Catherine York – US EPA Region 4
  Chelsea Weiskerger – US EPA Region 4

## Slide 5: US EPA Disclaimer
Although this work was reviewed by EPA and approved for presentation, it may not necessarily reflect official Agency policy.
Mention of trade names or commercial products does not constitute endorsement or recommendation for use.

## Slide 6: Class Introductions
Who you are?
Who do you work for?
What do want to get from this class?
Do you have a particular project?

## Slide 7: Course Objectives
Modeling Principles
Modeling Theory
  Processes in WASP
  Limitations of process descriptions
Modeling Practice
  Using the WASP Interface
  Using WASP for real-world problems
    Case Study Applications of WASP
    Discussion of Data Needs

## Slide 8: History
1970’s Developed by HydroScience
1983 Brought to EPA by Bob Ambrose
1985 Ported to IBM XT (MS DOS)
1994 WASP Graphical User Interface and Post Processor by AScI Corp
1999 Development of the Hydrodynamic Linkage API
2001 WASP 7 Released geared toward supporting TMDL Program
2001 to Current Numerous Upgrades to model
  3 Algal Classes, 3 BOD Classes, Benthic Algae, Sediment Diagenesis, pH/Alkalinity, linkage tools, post processing
2016 WASP8
2017 WASP8.1
2019 WASP8.3
2023 WASP 8.41

## Slide 9: WASP 8
Modernization of the User Interface
  Developed using Open Source Environment
  Improved Linkages to external database
  Improved Efficiency
Model
  Dynamic Allocation of Memory
  User Controlled Variable Complexity
  Improved Runtime Performance
  Improved Post Processing Performance

## Slide 10: WASP 8
Now Available in 64-Bit Distribution
Supports Multiple Operating Systems
  Windows (XP and Higher)
  Apple OSX (Yosemite or Higher)
  Linux

## Slide 11: Let’s Refresh
Why Model?

## Slide 12: Let’s Take a Step Back
Remember all Models are WRONG . . . (Not Quite True)
  They are a simplistic representation of reality
  They are tool that can be used to make an informed decision
  They have to be “Proven” to be useful

## Slide 13: Utility of Models
Models are Tools that:
  Can aid in the decision process
    TMDL
    Waste Load Allocation
    Numeric Nutrient Criteria
    Development of Best Management Practices

## Slide 14: Model Principles

## Slide 15: Mass and Concentration
c =
m
V
m = mass
V = volume
M
L3
units:

## Slide 16
Our First Model
WTP
Waste removed
CITY
Waste loading, W [M/T]
Critical concentration, c [M/L3]
WWTP
River
Remember:
W=Qc ?
Assumption:
7Q10 Flow = 1 cms
Water Quality Standard
5 mg/L
TMDL or WLA = Flow * Concentration
TMDL or WLA = 1 * 5 = 5 grams/second or 5 g/sec * 86400 sec/day = 432,000 g/day

## Slide 17
Assimilation Factor
c = W
1
a
1
a
W
c
system
stimulus
response
physics, chemistry, biology

## Slide 18
Modeling Modes
Simulation Mode: Given load (W) and assimilation
factor (a), calculate
Assimilative Capacity Design Model: Given desired
concentration (c) and assimilation factor (a), calculate
Environmental Modification Design Mode: Given desired concentration (c) and load (W), calculate

## Slide 19
How Do We Determine “a” ?
“a”?
EMPIRICAL
Data-based
(Inductive)
Model
MECHANISTIC
Theory-based
(Deductive)
Model

## Slide 20
c = W
a
1
physics, chemistry, biology
Transport and Kinetics
Transport
Kinetics

## Slide 21: Model Approaches
Statistical

## Slide 22
Empirical Models
W
c

## Slide 23: Multiple Regression
Multiple linear regression attempts to model the relationship between two or more explanatory variables and a response variable by fitting a linear equation to observed data.

## Slide 25: Bayesian Analysis
Bayesian statistics is a subset of the field of statistics in which the evidence about the true state of the world is expressed in terms of degrees of belief or, more specifically, Bayesian probabilities. Such an interpretation is only one of a number of interpretations of probability and there are other statistical techniques that are not based on "degrees of belief".

## Slide 26: Statistical -- Regression
Pro’s
Easily done
Links stressors to response variables
Uses site specific data for the waterbody
Con’s
May not account for all response variables
Constrained by the data availability
Confidence in the statistical fit
Difficult to extrapolate to other conditions
May not protect downstream

## Slide 27: Model Approaches
Mechanistic

## Slide 28: Mechanistic Models
Mechanistic Models are based on:
  Fundamental equations that produce physical/chemical/biological responses based on stressors (temporal and spatial)
  Many of the fundamental relationship were developed using direct observation

## Slide 29
Mechanistic Models
Conservation of Mass
source
sink
Volume
over a unit time period:
For a finite volume
(accumulation)
= (sources)
 (sinks)
accumulation
Mass Balance:

## Slide 30
Accumulation Mass
Steady State
Steady-state & Transient Solutions
sources = sinks 0 constant
Transient
sources > sinks
+ increases
sources < sinks - decreases

## Slide 31
W
Qc
kVc
vAc
V
dc
dt
V
dc
dt
=
accumulation = load  outflow  reaction  settling
Mass-Balance Equation
W  Qc  kVc vAc

## Slide 32: Utility of Mechanistic Models
Simplistic Representation of Reality
  Cannot Simulate “Everything”
  All Models are Wrong . . . .
Interpolate
  Known and Unknown
Provides Linkage between
  Loads and Response Variables
Can Determine Important Processes
  Nutrients/DO/Algae/Light
  Management Strategies
Determine Load Reductions to meet WQS
  Never to Exceed
  X% Exceedence
  Duration, Frequency and Magnitude
Evaluate Best Management Practices

## Slide 33: Using Mechanistic Models for TMDL
Critical Conditions (Steady State)
  Typically used for criteria development
Nutrients
  Usually not a critical condition
  Seasonal Variation
  Need to consider varying meteorological conditions
    Low/Ave/High Flow years
    Long-term Continuous Simulation
    Should allow perturbations

## Slide 34: Mechanistic Modeling
Pro’s
Linkage between stressors and response variables
  Chlorophyll a (algae, benthic algae, macrophytes)
  Light
  Dissolved Oxygen
Can Extrapolate
  Environmental Conditions
  Current vs. WQS Condition
  Response in Time
  Duration and Frequency
Con’s
Time consuming
Costly
Can be misapplied

## Slide 35: Introduction to WASP

## Slide 36
WASP
Input
BMD
Eutrophication
WRDB Graph
Stored
Data
Hydro
Model Preprocessor/Data Server
Binary Model Output
Graphical Post Processor
Models
Hydrodynamic
Interface
Exported Model Results
Messages
CSV, ASCII Output
Toxicants
Binary Wasp Input File (wif)
Metal Speciation
WASP8 Model Framework

## Slide 37: Box Model Approach
Numerical solution allows greater flexibility as to processes considered (i.e. eutrophication, toxics, etc.)
Allows greater flexibility as to segmentation (1/2 or 3 Dimensions)
Descriptive Transport based upon Field Data
Predictive Transport based upon Watershed Runoff and Routed using channel morphometry
Linked Transport with Hydrodynamic Models

## Slide 38: WASP8 Water Quality Modules
Advanced Eutrophication (MultiAlgae.dll)
  Nutrients, DO, Multiple CBOD, Multiple Phytoplankton, Multiple Periphyton/Macroalgae, Multiple Solids, Bacteria, Temperature, Sediment Diagenesis
Toxicant (toxi.dll)
  Multiple Chemicals, Multiple Nano Chemicals, Multiple Solids, Multiple Nano Solids, DOC, Partitioning, degradation, reaction yields
Metal Speciation
  Not available yet

## Slide 39: WASP Structure
WASP
Transport
Bookkeeping
Kinetics
Organic Chemical Model
Eutrophication Model
This allows model networks to be used for all WASP Scientific Modules

## Slide 40: WASP Terminology
Segments
Systems (i.e., State Variables)
NH3
NO3
DO
BOD
Chla
OPO4
Etc.
Calculated Variables
BOD Decay Rate
Growth Rate, etc.
1
2
3
4
5
6

## Slide 41: WASP Advantages and Features
Network Flexibility
  Applicable to most water body types at some level of complexity
Most Water Quality Problems
  Conventional Water Quality: DO, Eutrophication, Temperature
  Toxicant Fate: Organic Chemicals, Nano Materials, Simple Metals, Mercury
Separation of Processes, which allows manipulation
  Transport
  Kinetics
Ability to Access Data from Databases, Spreadsheets, other Models
Three Solution Techniques
  Simple/Quick – Euler
  Complex/Flux Limiting – COSMIC
  Intermediate – Runge-Kutta

## Slide 42: WASP Limitations
Does not handle some variables and processes:
  Mixing zone processes
  Non aqueous phase liquids (e.g., oil spills)
  Metals speciation reactions (special module, META4, not part of general WASP release)

## Slide 43: Development of Complexity in Water Quality Modeling Applications
Dominic Di Toro
Water Quality Modeling is more like . . . .

## Slide 44: WASP Modeling Framework
Does not Assume what you want to do
  Select the Module (Eutrophication or Toxicants)
  Select Module State Variables to meet the level of complexity
    Simple First Order Decay
    Streeter-Phelps
  WASP does not require you to use everything

## Slide 45: WASP is a Variable Complexity Modeling System
When building a water body model, adjust complexity to match the problem.
  More Complex Aquatic Systems
  More Complex Chemical Behavior
  More Complex Management Questions

## Slide 46: How Complex Should Final Computational Model Be?
Proper model complexity is driven by:
  The complexity of the environmental system.
  The complexity of the pollutants of concern.
  The management questions and related need for accuracy.
Consequences for overly simple model:
  Miss key processes and extrapolate inaccurately.
  May not address relevant management questions.
  May not be defensible to adversarial review.
  Insufficiently adaptable to changing management requirements.
Consequences for overly complex model:
  Adds unnecessary data collection and computational burdens.
  Adds to uncertainty.
  Shifts focus away from problem solutions to endless analysis.

## Slide 47: Goal of Model Complexity
Albert Einstein
“Make things as simple as possible,
but not any simpler.”

## Slide 48: A Final Word
“Do what you love and love what you do, and you’ll never work again.”

## Slide 49: Introduction to WASP Video

## Slide 50: Questions ?
Alex Comer Tim Wool Bob Ambrose James Martin