## Slide 1: Introduction to WASP8 Advanced Toxicant Module

## Slide 2
https://www.epa.gov/goldkingmine/fate-transport-analysis
Preface: Gold King Mine
The Gold King Mine is one of 100s of inactive mines in the Colorado mountains
On August 5, 2015, EPA was investigating the Gold King Mine near Silverton, CO
~ 3 million gallons of acid mine drainage released into Cement Creek, CO
~ 400,000 kg of metals entered the Animas River
https://www.youtube.com/watch?v=qBPO28FTawQ

## Slide 3
Preface: Gold King Mine

## Slide 4
Advanced Toxicant Module designed to handle range of toxicants
Metals
  Copper, Lead, Zinc, Cadmium
  Arsenic, Tin, Selenium, Chromium
Mercury
  Elemental, Divalent, Methyl
Solute Chemicals
  MTBE, PCBs
  Petroleum, BTEX, PAHs, Chlorinated Solvents, VOCs
  Pesticides, Organic Acids, PFAS
Nanomaterials
  Graphene Oxide, Copper Oxide, Multi-walled Carbon Nanotubes

## Slide 5
State Variables | Examples | Example Governing Processes
1-10+ Solids | Sand, Silt, Clay, Particulate Organic Matter, Algae | Settling, Deposition, Erosion, Resuspension, Bed Load, Growth, Decay
1-10+ Solute Chemicals | MTBE, PAHs, PCBs, BTEX, PFAS/PFOS, Chlorinated Solvents, VOCs, Organic Acids, Pesticides, Metals | Oxidation, Reduction, Biodegradation, Partitioning, Ionization, Volatilization Phototransformation
1-10+ Nanomaterials | Graphene Oxide, Carbon Nanotubes, Copper Oxide, Iron Oxide, Nano Silver | Decay, Phototransformation, Particle Attachment
1-5+ Dissolved Organic Carbon | Labile, semi-labile, semi-recalcitrant, recalcitrant | Decay, Complexation
Mercury | Elemental mercury (Hg0), Divalent mercury (HgII), Legacy divalent mercury (HgII), Methyl mercury (MeHg) | Oxidation, Reduction, Methylation, Demethylation, Photo-demethylation Volatilization, Particle Attachment
Pathogens | Escherichia coli | Decay, Photo-driven Decay, Particle Attachment

## Slide 6
PROCESSES
Dissolution
(2) Sorption
(3) Complexation
(4) Heteroaggregation
(5) Sedimentation
(6) Resuspension
(7) Diffusion
(8) Burial
(9) Advection
ACS EST Water 2022, 2, 9, 1532-1543
Simulating release of Nano Copper Oxide From Boats in a well-mixed lake

## Slide 7: Solute Chemicals Modeling
Processes
Photo-transformation
Biodegradation
Oxidation
Reduction
Ionization
Volatilization
Sorption
DOC complexation
Advection
Dispersion

## Slide 8
8
Volatilization
  Two film theory
  Mass Transfer
    Driven by wind
    Driven by water flow velocity
Sorption: Particle Attachment
  Equilibrium Partitioning
  Kinetic sorption
Solute Chemical Processes
water
air

## Slide 9
9
Reactions
  First Order Decay
  Photo-transformation
    Requires Light Module
  Biodegradation
    Zero order
    First Order
    Monod
    Second Order
  Oxidation - Reduction
Solute Chemical Processes
Photodegradation
Biodegradation
Oxidation
Reduction
O
O
COOH
COOH
OH
OH

## Slide 10
10
Solute Chemical Processes
=
kreaction Overall reaction rate constant (d-1), WASP8 internally calculates
krate Reaction rate constant specified by WASP users (d-1) at 20°C
Xtemp Temperature correction (q, Q10)
Xseg Segment factor (allows each segment to have different rate constant)
Xseg Segment type (water, surface sediment, deep sediment)
Xphase Phase multiplication factor
Xmon_subs Monod kinetic equation for substrate (half saturation constant)
Xmon_env Monod environmental factors (bacteria, oxidants, reductants)
*Default sets all to 1
General Reaction Model: Product of factors

## Slide 11: Solids Modeling
* Mechanistic solids only
Processes
Settling
Resuspension
Deposition
Erosion
Bed Load
Burial
Growth
Decay
2 main options
Descriptive
Mechanistic
Biomass
Growth
Death
Decay and dissolution

## Slide 12: Average Solids Transport Rates from Observations and Mass Balance
Surface Water
Surface Sediment
Subsurface Sediment
vs,silt
vr,silt
vb1,silt
SW
SB1,silt
vs = settling velocity, m/d
vr = resuspension velocity, m/d
vb = burial velocity, m/d
Sw = suspended solids conc, g/m3
(TSS, each solid type)
SB = sediment solids conc, g/m3
(TSS, each solid type)
Mass Balance Components:
vb2,silt
silt
clay
vs,clay
vr,clay
SB1,clay
SB1,sand
SB2,clay
SB2,sand
SB2,silt
vb2,clay
vb2,sand

## Slide 13: Light and Photoreactions
Solar Radiation travels and attenuates through atmosphere, changes over the day and throughout year
Light attenuates through the water column varying by wavelength
Each WASP segment has its own attenuation coefficient
Photo-transformation rates are a function of wavelength intensity
11 bands of wavelengths of light
  UVB (med and high)
  UVA (low, med, and high)
  Violet
  Blue
  Green
  Yellow-orange
  Red
  Infrared

## Slide 14: Division of Wavelengths by Latitude
Index | Color | Wavelengths [nm] | 0o N | 10 o N | 20 o N | Latitude 30 o N | 40 o N | 50 o N | 60 o N
1 | UVB med | 295 – 304 | 0.00015 | 0.00015 | 0.00013 | 0.00011 | 0.00008 | 0.00006 | 0.00004
2 | UVB high | 305 – 314 | 0.00142 | 0.00139 | 0.00132 | 0.00120 | 0.00104 | 0.00085 | 0.00067
3 | UVA low | 315 – 334 | 0.00845 | 0.00839 | 0.00825 | 0.00801 | 0.00766 | 0.00721 | 0.00681
4 | UVA med | 335 – 354 | 0.01141 | 0.01137 | 0.01126 | 0.01108 | 0.01082 | 0.01052 | 0.01054
5 | UVA high | 355 – 379 | 0.01723 | 0.01718 | 0.01706 | 0.01686 | 0.01655 | 0.01619 | 0.01630
6 | violet | 380 – 449 | 0.07626 | 0.07617 | 0.07593 | 0.07550 | 0.07482 | 0.07394 | 0.07443
7 | blue | 450 – 494 | 0.06664 | 0.06663 | 0.06659 | 0.06652 | 0.06639 | 0.06616 | 0.06644
8 | green | 495 – 569 | 0.10386 | 0.10388 | 0.10394 | 0.10402 | 0.10406 | 0.10390 | 0.10285
9 | yellow-orange | 570 – 619 | 0.06546 | 0.06549 | 0.06556 | 0.06566 | 0.06576 | 0.06568 | 0.06422
10 | red | 620 – 749 | 0.14914 | 0.14934 | 0.14995 | 0.15106 | 0.15282 | 0.15550 | 0.15769

## Slide 15: Light and Photoreactions
Solar Radiation travels and attenuates through atmosphere, changes over the day and throughout year
Light Options in WASP
  0: Model calculates clear sky radiation
    Based on user-specified latitude, longitude, and Julian day
  1: User specifies time series of instantaneous solar radiation
    Hourly or less time scale
  2: User specifies time series of daily total solar radiation
    Daylight fraction can be specified or calculated internally
    Model calculates diel variation using half-sine curve
User may need to include cloud cover.

## Slide 16: Light and Photoreactions
Light attenuates through the water column varying by wavelength
Beer-Lambert Law for attenuation of Light
Ke ,λ = net light extinction for WASP segment
Ke, Water,λ = light extinction of water
Ke, Chl,λ = algal self shading
Ke, DOC,λ = DOC light extinction
Ke, Solids,λ = solids light extinction
+
Photoreaction rate constant

## Slide 17: Using the Advanced Toxicant Module
Develop conceptual model of system
Develop physical layout: segments & hydrology
Add sediment layers
  number of sediment layers per water column
  Add solids, calibrate so sediment layers stabilize/match observed
Add light and/or water temperature – based on conceptual model
Once these are all working and calibrated
THEN add environmental contaminants and their processes

## Slide 18: Gold King Mine
Aug 5, 2015. 3 000 000 gal of acid mine drainage released from Gold King Mine
Release mobilized a large mass of solids, colloids, and dissolved metals
Low pH of release, pH of plume increased moving downstream
https://www.epa.gov/goldkingmine
“Analysis of the Transport and Fate of Metals Released from The Gold King Mine in the Animas and San Juan Rivers”
https://www.epa.gov/goldkingmine/fate-transport-analysis

## Slide 19: Model Domain
229 surface water 229 sediment
Mean length:
2447 m
Range:
922 – 4655 m

## Slide 20: Conceptual Model

## Slide 21: Plume Movement

## Slide 22: Total Metals: Peak Concentrations

## Slide 23: Individual Metals: Peak Concentrations

## Slide 24: Black Butte Mercury Mine
Deposit: primarily cinnabar​
​
Operation timeframe: 1890 to late 1960s​
1990s: purchased by Land & Timber Company​
​
Mine: underground mine; surface waste rock & tailings​
​
Ore Processing: elemental mercury was produced on the site by heating crushed ore in a furnace.​
New furnace constructed in 1927.​
​
Production: ~635,000 kg of Hg
Black Butte Mine

## Slide 25: Surface Waters impacted by Mercury Mine
Hg
Hg
River
Reservoir
MeHg
Permanently Inundated Pool
Seasonally Inundated Pool
Wetlands
River

## Slide 26: Surface Waters impacted by Mercury Mine
First order base reaction rate constants for mercury transformation processes. |  |  | 
Process | water [d-1] | surface sediment [d-1] | deep sediment [d-1]
methylation (HgII -> MeHg) | 0 | 0.0031a | 0
demethylation (MeHg -> HgII) | 0.01c | 0.25b | 0.1d
reduction (HgII -> Hg0) | 0.001e | 0 | 0
photo-demethylation (MeHg -> Hg0) | 0.03 f | 0 | 0
photo-reduction (HgII -> Hg0) | 0.03g | 0 | 0
photo-oxidation (Hg0 -> HgII) | 0.06h | 0 | 0
Partition and Complexation Coefficientsi |  |  | 
 | DOC | Silt | Clay
divalent mercury | 2x106 | 2.3x104 | 2.3x106
strongly bound divalent mercuryj | 0 | 2.28 x106 | 2.28x107
Methylmercury | 1.66x106 | 1.66 x104 | 1.66 x106
a observed methylation rate constant of 0.0045 d-1 (12h) and 0.0017 d-1 (24h). average rate constant 0.0031 d-1
b observed ratio of methylmercury to total mercury in sediments was 0.012, demethylation rate constant is estimated by dividing observed methylation rate constant by 0.012.
c based on literature values (Matilainen and Verta, 1995, Knightes et al., 2009)
d based on literature values (Benoit et all, 2003; Heyes et al., 2006; Hintelmann et al., 2000; Sunderland et al., 2004)
e based on literature values (Mason et al., 1995; O’Driscoll, et al., 2003)
f based on observed OU2 photodemethylation assay
g based on literature values (Amyot et al., 2000)
h based on literature values (LaLonde et al., 2001)
I calculated/estimated using observed data
J estimated as 100 times higher.

## Slide 27: Surface Waters impacted by Mercury Mine

## Slide 28: Surface Waters impacted by Mercury Mine
3 dimensional EFDC grid

## Slide 29: Surface Waters impacted by Mercury Mine
Preliminary results in Reservoir (do not cite)

## Slide 30: Carbon-based Nanomaterials in Freshwaters
Hypothetical Release of Multi-Walled Carbon Nanotubes(MWCNT) and Graphene Oxide (GO) (0.1 kg/d)
Sites:
Lake Waccamaw, NC – well mixed, wetland lake
Lake Barco, FL – seepage lake
Brier Creek, GA – coastal plans river
Yadkin River, NC – piedmont river

## Slide 31
PFAS (per- and polyfluoroalkyl substances)
perfluoroalkyl acids,
perfluoroalkylether acids,
  and their precursors
fluoropolymers,
perfluoropolyethers;
and other PFAS
Kwiatkowski et al. 2020. Scientific Basis for Managing PFAS as a Chemical Class. Environmental Science & Technology Letters 7 (8), 532-543. DOI: 10.1021/acs.estlett.0c00255

## Slide 33
Cove
Bay
Upstream boundary
Water column
Surface sediment
Deep sediment
From Cashman, et al., In Preparation
Water Column Samples
TSS & 18 PFAS
Sediment trap samples
sediment density,
total and pore water PFAS
Samples every 2 weeks for a year

## Slide 34
Acronym | Chemical Name | Formula | PFAS Type | Carbon-Chain Length
PFBA | Perfluorobutanoic acid | C4HF7O2 | PFCA | 4
PFPeA | Perfluoropentanoic acid | C5HF9O2 | PFCA | 5
PFHxA | Perfluorohexanoic acid | C6HF11O2 | PFCA | 6
PFHpA | Perfluoroheptanoic acid | C7HF13O2 | PFCA | 7
PFOA | Perfluorooctanoic acid | C8HF15O2 | PFCA | 8
PFNA | Perfluorononanoic acid | C9HF17O2 | PFCA | 9
PFDA | Perfluorodecanoic acid | C10HF19O2 | PFCA | 10
PFUnDA | Perfluoroundecanoic acid | C11HF21O2 | PFCA | 11
PFDoDA | Perfluorododecanoic acid | C12HF23O2 | PFCA | 12
PFTrDA | Perfluorotridecanoic acid | C13HF25O2 | PFCA | 13
PFTeDA | Perfluorotetradecanoic acid | C14HF27O2 | PFCA | 14
PFBS | Perfluorobutane sulfonic acid | C4HF9O3S | PFSA | 4
PFPeS | Perfluoropentane sulfonic acid | C5HF11O3S | PFSA | 5
PFHxS | Perfluorohexane sulfonic acid | C6HF13O3S | PFSA | 6
PFHpS | Perfluoroheptane sulfonic acid | C7HF15O3S | PFSA | 7
PFOS | Perfluorooctane sulfonic acid | C8HF17O3S | PFSA | 8
PFNS | Perfluorononane sulfonic acid | C9HF19O3S | PFSA | 9
PFDS | Perfluorodecane sulfonic acid | C10HF21O3S | PFSA | 10
4:2-FTS | 4:2 Fluorotelomer sulfonic acid | C6H5F9O3S | X:2 FTS | 6
6:2-FTS | 6:2 Fluorotelomer sulfonic acid | C8H5F13O3S | X:2 FTS | 8
8:2-FTS | 8:2 Fluorotelomer sulfonic acid | C10H5F17O3S | X:2 FTS | 10
FOSA | Perfluorooctanesulfonamide | C8H2F17NO2S | FASA | 8
N-MeFOSAA | 2-(N-methylperfluorooctane sulfonamido)acetic acid | C11H6F17NO4S | FASAA | 11
N-EtFOSAA | N-ethylperfluorooctane sulfonamidoacetic acid | C12H8F17NO4S | FASAA | 12

## Slide 35
Chart: log Kd
0.8 g total mass
31.3 ng/L total
31.0 ng/L dissolved
0.3 ng/L particulate
30.7 g/d total
30.5 g/d dissolved
0.2 g/d particulate
30.7 g/d total
30.4 g/d dissolved
0.3 g/d particulate
59 mg/d
10.4 mg/d
5.24 g
0.7 mg/d
surface sediments
Estuary Inflow
Into Bay
Cove
From Cashman, et al., In Preparation

## Slide 36
Chart: log Kd
From
Cashman, et al., In Preparation

## Slide 37: References
Advanced Toxicant
Knightes, Christopher D., Ambrose, R.B., Jr., Avant, B., Han, Y., Acrey, B., Bouchard, D.C., Zepp, R., Wool, T. 2019. Modeling framework for simulating concentrations of solute chemicals, nanoparticles, and solids in surface waters and sediments: WASP8 Advanced Toxicant Module. Environmental Modelling & Software. 111: 444-458, https://doi.org/10.1016/j.envsoft.2018.10.012.
Nanomaterials
Avant, Brian, Bouchard, D., Chang, X., Hsieh, H.S., Acrey, B., Han, Y., Spear, J., Zepp, R. and Knightes, C.D., 2019. Environmental fate of multiwalled carbon nanotubes and graphene oxide across different aquatic ecosystems. NanoImpact. doi.org/10.1016/j.impact.2018.11.001
Bouchard, D.C., Knightes, C.D., Chang, X., Avant, B. 2017 Simulating Multiwalled Carbon Nanotube Transport in Surface Water Systems Using the Water Quality Analysis Simulation Program (WASP). Environmental Science & Technology. DOI: 10.1021/acs.est.7b01477
Han, Yanlai, Knightes, C.D., Bouchard, D., Zepp, R., Avant, B., Hsien, H.-S., Chang, X., Acrey, B., Henderson, M.W., Spear. J. 2019. Simulating graphene oxide nanomaterial phototransformation and transport in surface water. Environmental Science: Nano. DOI: 10.1039/C8EN01088A.
Ross, B.N., Knightes, C.D. 2022. Simulation of the environmental fate and transport of nano copper oxide in a freshwater environment. ACS ES&T Water. 2(9): 1532-1543. DOI: 10.1021/acsestwater.2c00157.
Mercury
Knightes, C.D., Sunderland, E.M., Barber, M.C. Johnston, J.M., Ambrose, R.B., Jr. 2009. Application of Ecosystem-Scale Fate and Bioaccumulation Models to Predict Fish Mercury Response Times to Changes in Atmospheric Deposition. Environmental Toxicology and Chemistry 28(4): 881–893.
Eckley, C.S., Luxton, T.P., Knightes, C.D., Shah, V. 2021. Methylmercury production and degradation under light and dark conditions in the water column of the Hells Canyon Reservoirs, USA. Environmental Toxicology and Chemistry. 40(7):1827-1837. https://doi.org/10.1002/etc.5041