## Slide 1: WASP8 Particle Attachment: Sorption Kinetic Partitioning Nanomaterial Heteroaggregation

## Slide 2
2
Particle attachment
Attachment to particles is an important governing process in environmental modeling
The transport of a chemical attached to a particle is governed by the processes governing the transport of the given particle
  Settling
  Deposition
  Resuspension
  Burial
Possibly isolate chemical from reactions requiring aqueous phase

## Slide 3
Chemical and Solids Cycling
Ross and Knightes, 2022, ACS ES&T Water
Flowing downstream, chemicals attach and detach from particles
When a chemical attaches to a solid, it then settles to the sediment layer
Chemicals then accumulate in the sediments and can act as a long-term source

## Slide 4
4
Particle attachment
WASP can simulate 3 types of particle attachment
Equilibrium
  Assumes instantaneous distribution of chemical across multiple solid phases
Kinetic sorption
  Particle attachment follows first order kinetics
  Takes time for chemical to attach (sorb) and detach (desorb)
Hetero-aggregation (nanomaterial to solid particle)
  Specific to nanomaterials
  Follows colloidal theory to simulate particle attachment of a nanomaterial following hetero-aggregation

## Slide 5
5
Equilibrium Partitioning
sand
silt
clay
DOC
Assumes partitioning is instantaneous
WASP calculates the fraction attached to every particle type and every form of DOC being simulated
For each time step for each segment, WASP calculates the fraction attached to each particle and simulates each according to its governing processes
Fraction of chemical, i, attached to particle, j

## Slide 6
6
Kinetic Sorption
clay
Kinetic sorption takes time for the chemical to attach to the particle
Sorption is modeled using second order kinetics, depending on chemical and solids concentration
Desorption is modeled as first order kinetics
Because of the kinetic nature of this process, WASP needs to have a state variable as the chemical attached to each solid
  Chemical and Chemical=solid

## Slide 7: Hetero-aggregation of Nanomaterials
7
khetagg = ahetagg x kcoll x Cspm
Brownian Motion
Fluid Motion
Differential Settling

## Slide 8: WASP8 Particle Attachment: in-class example

## Slide 9
Add Benzene load into River-Lake-Solids model
Loads
Benzene time varying load
1/1/00 to 5/31/00: 0 kg/d
6/1/00 to 5/31/05: 20 kg/d
6/1/05 to 1/1/10: 0 kg/d

## Slide 10
Add Benzene load into River-Lake-Solids model
Parameters
Chemical: Turn on Chemical Partition Coefficient multiplier. Set to 1

## Slide 11
Add Benzene load into River-Lake-Solids model
Constants
Chemical Properties
Molecular weight: 464

## Slide 12
Add Benzene load into River-Lake-Solids model
Constants
Chemical Partitioning
Partitioning Coefficient
To Solid(1) [sand] 10 L/kg
To Solid(2) [silt] 1000 L/kg

## Slide 13
Total and Dissolved Benzene in the Epilimnion

## Slide 14
Total and Dissolved Benzene in the Hypolimnion

## Slide 15
Total and Dissolved Benzene in the Surface Lake Sediments