## Slide 1: WASP8 Class Example: River – Lake - Solids

## Slide 2: River -> Lake - with Sediments
10 layer system, depths
  3 surface water, 1.5 m
  1 subsurface water, 1 m
  3 surface sediment, 2 cm
  3 subsurface sediment, 5 cm
Inflow
  Water, 104 m3/d
  Silt, 10 mg/L (BC)
  Sand, 40 kg/d
Ponded weir at lake boundary
Settling, 0.5 m/d
Resuspension, 0.05 mm/d
Silt

## Slide 3: Dataset Parameters
Advanced Toxicant
Set Time Range
  1/1/2000 12:00 PM
  1/1/2010 12:00 PM
Time Step
  Fraction of Max DT = 0.9
  Max Allowable Timestep:1 d
  Min Allowable Timestep: 0.00001 d
  Model Output Interval: 5 d
Bed Volumes
  Dynamic
  Bed Compaction Time Step: 1.0 d

## Slide 4
Systems
Model State Variable Activation
SOLID 1 = sand
  Density = 2.65 g/cm3
SOLID 2 = silt
  Density = 2.65 g/cm3

## Slide 5
Segments
Segment Definition
Enter each segment name
Define the segment Type
Define the transport mode
Describe the segments below
  For light attenuation
  Solids movement
    Settling
    Resuspension

## Slide 6
Segments
Initial Conditions
Units: g/m3 (mg/L)
Sediment layers
  0 mg/L
Sediment layers
  Sand 318,000 g/m3
  Silt 212,000 g/m3

## Slide 7
Parameters
Solids
Silt Solid Settling Velocity: Scale Factor: 1 ; All water segments = 0.5 m/d
Silt Solid Resuspension Velocity: Scale Factor 1e-05 m/d, all surface sediments = 1

## Slide 8
Constants
Solids Transport
Solids Option: 0
Particle Diameter
  Sand = 4 mm
  Silt = 0.004 mm

## Slide 9
Exchanges
Surface Water
Used
Exchange Function:
  3: Lake Epilimnion to 4: Lake_Hypolimnion
  Area: 30,000 m2
  Distance: 1.5 m
  Value: 1e-06 m2/s

## Slide 10
Exchanges
Pore Water
Used
Exchange Function:
  Link water column to surface sediment
  Link surface sediment to subsurface sediment
River Exchange Area:
  5,000 m2
River Exchange Distance:
  0.01 m
River Exchange Area:
  30,000 m2
River Exchange Distance:
  0.035 m

## Slide 11
Flows
Channel Geometry

## Slide 12
Flows
Surface Water
Flow Function
Flow Path
Flow Value 0.1 m3/s

## Slide 13
Boundaries and Loads
Boundaries
Silt Boundary
10 mg/L

## Slide 14
Boundaries and Loads
Loads
Sand into Surface Seds
40 kg/d

## Slide 15
Solids Concentrations in Lake Surface

## Slide 16
Burial Velocity in Subsurface Lake Sediments