## Slide 1: WASP8 Advanced Toxicant Module: Gas Transfer (Volatilization/Reaeration)

## Slide 2: Introduction
Volatilization theory (background)
How WASP calculates volatilization
Instructions on how two implement volatilization in WASP8

## Slide 3: Volatilization theory
Mass transfer is a bi-directional process
Mass moves towards the lower concentration
O2
O2
O2
O2
O2
O2
O2
Reaeration
Oxygen moving into water
Hg0
Volatilization
Hg0 moving out of water
Hg0
Hg0
Hg0
Hg0
Hg0
Hg0
Hg0
Volatilization
Benzene moving out of water

## Slide 4: Two Film Theory of Mass Transfer
Mass transfer limited two layers:
  water film and air film
Mass flux through water film
Mass flux through air film
Whitman’s two-film theory
bulk air
air film
water film
bulk water
Ci
Ci
Cair
Cw
air-water
interface
Ji = mass flux (mol m2 d-1)
ki = mass transfer velocity (m d-1)
Ci = aqueous concentration (mol m-3)
pi = partial pressure (atm)
R = universal gas constant (atm m3 mol-1 K-1)
H = Henry’s law constant (atm m3 mol-1)

## Slide 5: Two Film Theory of Mass Transfer
Net mass transfer can be written as
= mass transfer coefficient (d-1)
Whitman’s two-film theory
bulk air
air film
water film
bulk water
Ci
Ci
Cair
Cw
air-water
interface
, air water partition coefficient (--)

## Slide 6
Water velocity driven gas transfer
WASP calculates gas transfer rate using the one of the following equations
O’Connor-Dobbins
Churchill et al.
Owens et al.
Wind velocity driven gas transfer options
O’Connor
MacKay
1
2
3
Covar, 1976;
Zison et al., 1978

## Slide 7: Gas Transfer Driving Force
Mass transfer depends on what is the driving force
Cair
Cdiss
Air
Water
Cair
Cdiss
Air
Water
Lakes and ponds
Rivers and Estuaries
Wind is driving force
Flow velocity is driving force

## Slide 8: Incorporating Gas Transfer in WASP - Example
Two Water Bodies, Two chemicals
2 Well mixed lakes, same volume
  One is deeper and less area than the other
2 chemicals:
  Elemental Mercury (Hg0)
  Benzene (C6H6)

## Slide 9
Data Set
Advanced Toxicant
Set Time Range
  1/1/2000 12:00 PM
  12/31/2000 12:00 PM
Time Step
  Fraction of Max DT = 0.9
  Max Allowable Timestep
    0.05 d
  Min Allowable Timestep
    0.00001 d
  Model Output Interval
    0.1 d

## Slide 10
Systems
Three State Variables
HG_0_ Elemental Mercury
CHEMI Benzene

## Slide 11
Segments
Segment Definition
Segment 1
  Segment Name Lake
  Segment Type: Surface Water
  Transport Mode: Stream Routing
Initial Conditions
  Elemental Mercury: 10 mg/L
  Benzene: 10 mg/L

## Slide 12
Flows
Channel Geometry
  Segment Name: Lake
  Volume: 3e+06 m3
  Length: 1200 m
  Average Width: 500 m
  Minimum Depth: 0.9 m
  Average Depth: 5 m
Surface Water
  Flow: 0 m3/s

## Slide 13
Parameters
Environmental
  Temperature of Segment
  Temperature Time Function
  Scale Factor for Wind
  Wind Speed Time Function

## Slide 14
Constants
General
  Water Body Type
  Latitude - degrees
  Longitude - degrees

## Slide 15
Constants
Chemical Properties (Benzene)
  Molecular weight: 464
  Henry’s Law: 0.152 atm/(mol/m3)
  Ratio of volatilization to reaeration: 1
  Wind driven volatilization option: 1
Mercury Properties (Hg0)
  Molecular weight: 201
  Henry’s Law: 0071 atm/(mol/m3)
  Ratio of volatilization to reaeration: 1
  Wind driven volatilization option: 1

## Slide 16
Time Functions
Water Temperature Function 1
Wind Speed Time Function 1

## Slide 17
Output Control
Chemical (Benzene)
  Total Chemical
  Chemical i Conc
  Volatilization rate constant
Mercury (Hg0)
  Total Hg Conc
  Elemental Hg Conc
  Hg0 volatilization rate

## Slide 18
Gas Transfer in WASP – Example 1

## Slide 19
Example 2
Half as wide (250m)
Twice as deep (10m)
Channel Geometry
  Segment Name: Lake
  Volume: 3e+06 m3
  Length: 1200 m
  Average Width: 250 m
  Minimum Depth: 0.9 m
  Average Depth: 10 m
Surface Water
  Flow: 0 m3/s

## Slide 20
Gas Transfer in WASP – Example 2

## Slide 21
Gas Transfer in WASP
Comparing two systems
Benzene
Mercury